| Air Force Navy القوة الجوية البحرية | AN |
| --- | --- |
| Military Standard المقياس أو المعيار العسكري | MS |
| National Aerospace Standard | NAS |
| Society of Automotive Engineering | SAE |

Type of (Rivet):

- Solid shank rivet

- Special rivet

Type of (Rivet head design):

| Flat head | AN 442 |
| --- | --- |
| Universal head | AN 470 |
| Counter sunk | AN 426 |
| Round head | AN 430 |

Type of Rivet Alloy (Code and Mark): حفظ الأشكال

- 1100  Aluminum (A)

- 2117  Aluminum alloy  (AD)

- 5056  Aluminum alloy  (B)

- 2017  Aluminum alloy  (D)

- 2024  Aluminum alloy  (DD)

- 7050T73 Aluminum alloy (E)

- Corrosion resistant steel   (F)

- Monel (M)

Type of (Special Rivet):

- Pop rivet

- Friction-lock rivet

- Mechanical-lock rivet

  - Huck-lock

  - Cherry-lock

  - Olympic-lock

  - Cherry max

ملاحظة هامة: الـicebox  هي عبارة عن ثلاجة يوضع فيها الـ2017(D) & 2024(DD)  لزيادة صلابتها

ما هو الشرط الأساسي الذي يجب إتخاذه عند إستبدال الـ Friction-lock مع الـ Solid Shank Rivet:

It must be at least one size (1/32 inch) larger in diameter. This is because a friction-lock rivet loses considerable strength if its center stems falls out due to damage

Example:

AN: Air Force Navy

430: Round head

AD: 2117 Aluminum alloy

4:     القطرD = 4/32

5:   الطول L = 5/16

Microshaver: this rotary cutter shaves the rivet head flush with the skin

Type of (Special Fasteners):

- Lock Bolts

- Hi-Loks:  لتركيبها hand tools  نستخدم الـ

- Hi-Lites

- CherryBucks

- Taper-Lok

- Hi-Tigue

- Jo-Bolts

Stump-Type Lockbolt: أين تستخدم

Is installed in places where there is not enough room to use the standard pulling tool, and used to install Hi-Shear Rivet

Type of (Bolt): حفظ دون أرقام

- Standard aircraft bolt AN3 – AN20

- Drilled-head engine bolts AN73 – AN81

- Close tolerance bolts AN173 – AN186

- Clevis bolt AN21 – AN36

- Internal wrenching bolt MS20004 – MS20024

Safety Procedures for (Removal of Rivets):

- Center punch the exact center of the manufactured head

- Drill through the head

- Cape chisel: to knock off the head

- Pin punch and a tipping motion: to break the rivet head

- Pin punch: to remove the shank rivet from the skin

Type of (Screw):

- Machine

- Self-tapping

- Structural

Type of (Pin):

- Roll pin

- Clevis pin

- Cotter pin

- Taper pin

Type of (Washer):

- Plain washer

- Lock washer

- Special washer

Type of (Turnlock Fasteners):  أنواع المثبتات التي تُغـْـلَـقُ بـِلَــفـِّـة

- Dzus fasteners

- Airloc fasteners

- Camlock fasteners

- هذه البراغي ربع لفه فقط تستخدم في الأماكن الحساسة مثل الـ doors أو غطاء محرك الطائرة cowling

Type of (Cable):

- Flexible  7×7

- Non-flexible  1×7 or 1×9

- Extra flexible 7×19

Advantage of (Cable):

- Linkages مترابط

- Strong قوي

- Light weight الوزن الخفيف

- Flexibility المرونة

- Easy to route سهل التوجيه

Problem with (Cable):

- Wear َيبلى بالإستعمال

- Corrosion

- Temperature

Type of (Terminals):

- Ball and double shank

- Ball and single shank

- Fork end

- Eye end

- Long threaded stud end

- Short threaded stud end

Turnbuckles: provide a means of adjusting control cables when they age and stretch

(Go/No-Go) gauge Or (before and after): to ensure that a terminal is properly swaged

# Text boxes

دائما نقسم الـ diameter على 32 والـ length على 16