Advisory Circular

AC No.:  135-16

Originator:  AFS-250

Date:  12/12/94

SUBJECT:  Ground Deicing and Anti-icing Training and Checking

1.  PURPOSE.  This advisory circular (AC) provides one means, but not the only means, of complying with Federal Aviation Regulations (FAR) Sections 135.227, 135.345, and 135.351 (referred to as the FAR Part 135 ground deicing rule).  Specifically, the guidance in this AC concerns:

a.  Ground deicing and anti-icing training requirements that should be incorporated into an approved training program for certain air carriers;

b.  Ground deicing and anti-icing guidance for those air carriers that are not required to have an approved training program;  and

c.  The pretakeoff contamination aircraft check required of all FAR Part 135 air carriers except those that develop an approved alternative procedure or comply with the FAR Part 121ground deicing rule contained in FAR Section 121.629(c).

2.  RELATED FAR SECTIONS.

a.  Part 135, Subpart A -- General.  Sections 135.23-25.

b.  Part 135, Subpart B -- Flight Operations.  Sections 			135.77-81.

c.  Part 135, Subpart D -- VFR/IFR Operating Limitations and 		Weather Requirements.  Section 135.227.

d.  Part 135, Subpart E -- Flight Crewmember Requirements. 			Section 135.244.

e.  Part 135, Subpart H -- Training.  Sections 135.323-329, 		135.339-347, and 135.351.

f.  Special Federal Aviation Regulation (SFAR) No. 58. 			Advanced Qualification Program.

3.  RELATED READING MATERIAL.  The following material should be useful in developing material, instructions, and procedures for incorporation in the certificate holder's training programs and operations manual:

a.  AC 20-117, Hazards Following Ground Deicing and Ground 		    Operations in Conditions Conducive to Aircraft Icing.

b.  AC 120-58, Pilot Guide for Large Aircraft Ground Deicing.

c.  AC 135-60, Ground Deicing and Anti-Icing Program.

d.  AC 135-17, Pilot Guide for Small Aircraft Ground Deicing.

e.  Federal Aviation Administration (FAA) publication, Winter 	    Operations Guidance for Air Carriers and Other Adverse Weather 	    Topics.

NOTE:  Copies of these documents may be obtained from the Department of Transportation, M-45.3,General Services Section, Washington, DC 20590.

f.  Society of Automotive Engineers (SAE):

(1) AMS 1424, Deicing/Anti-Icing Fluid, Aircraft, 				  Newtonian -- SAE Type I.

(2) AMS 1428, Fluid, Aircraft Deicing/Anti-Icing,

Non-Newtonian, Pseudo-Plastic, SAE Type II.

(3) ARP 4737, Aircraft Deicing/Anti-Icing Methods with 				  Fluids, for Large Transport Aircraft.

NOTE:  Copies of the SAE documents may be obtained by writing to the Society of Automotive Engineers, 400 Commonwealth Drive, Warrendale, Pennsylvania 15096-0001.

g.  International Standards Organization (ISO)publications:

(1) ISO 11075, Aerospace -- Aircraft Deicing/Anti-Icing

Newtonian Fluids ISO Type I.

(2) ISO 11076, Aerospace -- Aircraft Deicing/Anti-Icing

Methods with Fluids.

(3) ISO 11077, Aerospace -- Deicing/Anti-Icing Self 				  Propelled Vehicles - Functional Requirements.

(4) ISO 11078, Aerospace -- Aircraft Deicing/Anti-Icing 			  Non-Newtonian Fluids ISO Type II.

NOTE:  Copies of the ISO documents may be obtained from American National Standards Institute, 11 West 42nd Street, New York, New York, 10036, (212) 642-4900.

4.  Background.

a.  The "Clean Aircraft" Concept.  The current regulations

in FAR Parts 121 and 135 rely on the "clean aircraft" concept;

i.e., that no person may takeoff an airplane when frost, ice, or

snow is adhering to the wings, control surfaces, or propellers of

the airplane (FAR Sections 121.629 and 135.227).  The rationale

behind this concept is that the presence of even minute amounts

of frost, ice, or snow (referred to as "contamination") on

particular airplane surfaces can cause a potentially dangerous

degradation of airplane performance and unexpected changes in

airplane flight characteristics.  Under current regulations,

ultimate responsibility for determining whether the airplane is

free of contamination and complies with the "clean aircraft"

concept rests with the pilot in command (PIC).  Both the FAA and

industry have developed guidance and recommended procedures that

are designed to help the PIC in making that determination.  These

procedures include monitoring weather conditions and temperature

changes, visual checks, and using deicing/anti-icing fluids.

When conditions conducive to the formation of frost, ice, or snow

on airplane surfaces exist at the time of takeoff, those surfaces

should be checked for contamination in accordance with FAR

Section 135.227.  When contaminants are adhering to airplane

surfaces, those contaminants, except as specifically provided for

in the rule, should be removed before takeoff.  Because of the

wide variations in airplane design and performance 	characteristics, methods for removing contamination for airplanes

operated under FAR Parts 121 and 135 vary greatly.  Deicing of

airplanes may be accomplished:

(1) By applying heated water followed by undiluted

glycol-based fluid;

(2) By applying a heated water/glycol solution;

(3) By mechanically brushing the snow or ice off; or

(4) By placing the airplane in a hangar until the

frost, ice, or snow melts.

Note:  Currently, anti-icing (the treatment of the airplane with undiluted (Type II) glycol-based fluid to prevent frost, ice, or snow from adhering to aircraft surfaces) is not commonly used in FAR Part 135 operations.

b.  Accidents Related to Icing.  National Transportation

Safety Board (NTSB) records reveal that 14 ground icing-related

accidents and incidents involving airplanes operating under FAR

Part 135 occurred during the period of 1984-1992.  While most of

these accidents/incidents involved FAR Part 135 nonscheduled

cargo operations, three involved passenger-carrying operations.

The NTSB identified other probable causes in some of these

accidents/incidents, but in all 14 cases the NTSB identified the

existence of frost, ice, or snow on the wings or other critical

surfaces of the airplane as a probable cause.  A common thread

throughout these accidents/incidents was the pilots' apparent

lack of awareness of the potential hazard from even small amounts

of frost, ice, or snow on an airplane's wings and control

surfaces.  For instance, one pilot lost his life in an accident

involving a nonscheduled cargo operation in Morrisonville, New

York, on March 19, 1984.  Prior to the accident, after

identifying the presence of ice accumulation on the leading edges

and upper wing surfaces, the pilot declined the use of a hangar

to warm the airplane and instead attempted to remove the ice from

the leading edges by hand.  In another accident in Vienna,

Missouri, on March 3, 1988, a pilot of a night cargo operation

and another person lost their lives after taking off in known

icing conditions.  Before the flight, a line serviceman noticed

ice on the aircraft's wings and suggested its removal, but the

pilot declined.

5.  DEFINITIONS.  The terms used in this AC are not defined in

FAR Part 1, but are defined herein for better understanding of

this material as follows:

a.  Deicing.  A procedure by which frost, ice, or snow is

removed from the aircraft in order to provide clean surfaces.

b.  Anti-Icing.  A precautionary procedure that provides

protection against the formation of frost or ice and accumulation

of snow on treated surfaces of the aircraft for a limited period

of time.

c.  Deicing/Anti-Icing.  A combination of the two

procedures above.  It can be performed in one or two steps.

(1)  One-step deicing/anti-icing is carried out with an

anti-icing fluid.  The fluid used to deice the aircraft remains

on aircraft surfaces to provide limited anti-ice capability.

(2)  Two-step deicing/anti-icing consists of two

distinct steps.  The first step (deicing) is followed by the

second step (anti-icing) as a separate fluid application.

Anti-icing fluid is applied to protect the relevant surfaces,

thus providing maximum possible anti-ice capability (holdover

time).

d.  Holdover Time.  The estimated time deicing or

anti-icing fluid will prevent the formation of frost or ice and

the accumulation of snow on the treated surfaces of an

aircraft.  Holdover time begins when the final application of

deicing/anti-icing fluid commences, and it expires when the

deicing/anti-icing fluid applied to the aircraft loses its

effectiveness.

e.  Pretakeoff Contamination Check.  A pretakeoff

contamination check is a check to make sure the wings and control

surfaces are free of frost, ice, or snow.  FAR Section 135.227

requires that a pretakeoff contamination check be completed

within 5 minutes prior to beginning takeoff.  Under FAR Part 135,

depending upon the type of aircraft, it may be accomplished from

within or outside the aircraft and may be visual or tactile or a

combination, as long as the check is adequate to ensure the

absence of contamination.  The certificate holder's FAA principal

operations inspector (POI) must approve the pretakeoff

contamination check procedures for each specific type of aircraft

operated by the certificate holder.  Also, the pretakeoff

contamination check is referenced or described within the

certificate holder's operations specifications.

6.  OVERVIEW OF THE FAR PART 135 GROUND DEICING RULE.  The FAA

and the aviation community rely almost exclusively on the PIC's

judgment for ensuring the clean aircraft concept.  The FAA

believes that pilot education is the paramount element to

combating the threat of icing.  After reassessing its policy and

reviewing accident statistics, the FAA still believes that pilot

education is a major element in combating these types of

accidents, but it should be supplemented by aircraft checks for

contamination.  To ensure the implementation of the clean

aircraft concept, the FAR Part 135 ground deicing rule requires

education through additional training, and an aircraft check for

contamination of the wings and control surfaces prior to

beginning takeoff.  All FAR Part 135 certificate holders whose

aircraft expect to takeoff in ground icing conditions should

complete a pretakeoff contamination check.  The FAR Part 135

ground deicing rule allows an operator to develop an approved

alternative method of checking the aircraft for contamination

such as use of approved ice detection technology.  Additionally,

FAR Part 135 certificate holders may comply with FAR Section

121.629(c) deicing program requirements.

7.  APPLICABILITY OF THE FAR PART 135 GROUND DEICING RULE.

a.  General.  The FAR Part 135 ground deicing rule

requires that deicing/anti-icing pilot training and pretakeoff

contamination check procedures or an approved alternative to the

pretakeoff contamination check (alternative aircraft check) be

incorporated into a certificate holder's approved training

program.  The procedures for a pretakeoff contamination check or

the alternative aircraft check should also be in the certificate

holder's operations manual and referenced in its operations

specifications.  Pretakeoff contamination check or alternative

aircraft check procedures will be fully described in the

operations specifications for those operators not required to

have an operations manual.  The FAR Part 135 ground deicing rule

does not apply to FAR Part 91 operations conducted by a Part 135

operator.

b.  FAR Part 135 Certificate Holder Who Complies with the

FAR Part 121 Ground Deicing Rule.  If approved, an FAR Part 135

operator can comply with the FAR Part 121 ground deicing rule.

However, the operator must comply with all the provisions of FAR

Section 121.629(c), including training requirements and not just

with selected provisions.

c.  Certificate Holders Who Use Only One Pilot in Their

Operations.  Certificate holders who use only one pilot in their

operations (single pilot operations) are not required to comply

with the manual and approved training program requirements in FAR

Sections 135.21, Manual Requirements, and 135.341, Pilot and

Flight Attendant Crewmember Training Programs.  Therefore, single

pilot operations are not required to have an approved pilot

training program nor the additional training required by the FAR

Part 135 ground deicing rule.  However, single pilot operations

must comply with all the operational requirements (i.e.,

pretakeoff contamination check or an approved alternative to the

pretakeoff contamination check described in its operations

specifications) of the FAR Part 135 ground deicing rule.  The

pilots of these types of operations will need to demonstrate the

knowledge required to operate in ground icing conditions during

initial and recurrent flight checks.  Thus, the information

contained in this AC is also applicable to certificate holders

who use only one pilot in their operations.

d.  Helicopter Operations.  Helicopters generally do not

operate in icing conditions.  The FAA's review of icing-related

accidents and incidents did not reveal any accident history for

helicopter operations that suggest additional training or a

special inspection requirement would be necessary.  Therefore,

helicopter operations conducted under FAR Part 135 are excluded

from the additional training and aircraft checking requirements

of the FAR Part 135 ground deicing rule.  However, the "clean

aircraft" concept still applies to helicopters.

e.  Certificate Holders In Areas of Operations Where

Ground Icing Conditions Are Not Likely To Be Encouraged.  Each

certificate holder may elect not to fly during ground icing

conditions.  Ground icing conditions are defined as any time

conditions are such that frost, ice, or snow may reasonably be

expected to adhere to the airplane.  The prohibition against

takeoffs in ground icing conditions will be specifically stated

in the certificate holder's operations specifications.

8.  MISCELLANEOUS.

a.  Associated Deicing/Anti-Icing Personnel (To Include

Contractors).  The ground deicing rule in FAR Part 135 requires

additional training for pilots only.  However, if the certificate

holder uses additional employees (i.e., maintenance mechanic,

ramp agent, service personnel, and contractors) to accomplish

deicing and anti-icing procedures, the certificate holder's

manuals will contain procedures for those personnel consistent

with FAR Sections 135.21 and 135.23.

9.  OPERATIONAL REQUIREMENT OF THE FAR PART 135 GROUND DEICING

RULE.

a.  Pretakeoff Contamination Check.  Except for those FAR

Part 135 certificate holders who voluntarily choose to comply

with the FAR Part 121 ground deicing rule or those that develop

an approved alternative procedure, each applicable air carrier

who operates under FAR Part 135 should develop approved

procedures for a pretakeoff contamination check of the aircraft.

As previously stated, the FAR Part 135 ground deice rule does not

apply to a certificate holder who does not operate in ground

icing conditions.  In accordance with FAR Section 135.227, the

certificate holder's POI should approve the pretakeoff

contamination check procedures for each specific type of aircraft

operated by the certificate holder.  Except for single pilot

operations, the procedures for a pretakeoff contamination check

should be contained in the certificate holder's approved training

program, operations manual, and referenced within the certificate

holder's operations specifications.  FAR Part 135 single pilot

operations will have the pretakeoff contamination procedures

described in its operations specifications.

b.  Alternative Procedure to the Pretakeoff Contamination

Check.  The Administrator may approve a certificate holder's

alternative procedure which ensures that wings and control

surfaces are free of frost, ice, or snow, instead of the

pretakeoff contamination check as set forth in this rule.  An

alternative procedure may include procedures, techniques, or

equipment (such as wing icing sensors) to establish that wings

and control surfaces are not contaminated.  Pretakeoff

contamination check or alternative aircraft check procedures will

be fully described in the operations specifications for those

operators not required to have an operations manual.  The FAR

Part 135 ground deicing rule does not apply to FAR Part 91

operations conducted by an FAR Part 135 operator.

c.  FAR Part 135 Certificate Holder Who Complies with the

FAR Part 121 Ground Deicing Rule.  The FAR Part 135 ground

deicing rule allows a certificate holder to comply with FAR

Section 121.629(c) program requirements.  Guidance for

development of an FAR Part 121 program is contained in AC 121-60.

10.  TRAINING REQUIREMENTS IN CERTIFICATE HOLDER'S APPROVED

TRAINING PROGRAM.  For certificate holders who are required to

have an approved training program and who anticipate takeoffs in

ground icing conditions, that training program should include

pilot ground training in those subjects relating to deicing and

anti-icing operations as required by FAR Section 135.345 for

initial, transition, and upgrade training and FAR Section 135.351

for recurrent training.  The training required by the regulation

include procedures for operating airplanes during ground icing

conditions.  That training should include at least the following

elements if applicable to the type of aircraft and methods of

deicing/anti-icing used.

a.  The use of holdover timetables when using

deicing/anti-icing fluids.

b.  Aircraft deicing/anti-icing procedures, including

inspection and check procedures and responsibilities.

c.  Communications procedures.

d.  Airplane surface contamination (i.e., adherence of

frost, snow, ice, or snow) and critical area identification, and

how contamination adversely affects airplane performance and

flight characteristics.

e.  Types and characteristics of deicing/anti-icing

fluids, if used by the certificate holder.

f.  Cold weather preflight inspection procedures.

g.  Techniques for recognizing contamination on the

airplane.

11.  USE OF HOLDOVER TIMETABLES WHEN USING DEICING/ANTI-ICING

FLUIDS.

a.  Use of Holdover Timetables.  Holdover times are only

an estimate of the time deicing/anti-icing fluid prevents the

formation of frost or ice and the accumulation of snow on the

treated surfaces of an aircraft.  A holdover time begins when the

final application of deicing/anti-icing fluid commences and

expires when the deicing/anti-icing fluid applied to the aircraft

loses its effectiveness as described in the appropriate holdover

timetable.  The effectiveness of deicing/anti-icing fluids are

based on a number of variables;  e.g., temperature, moisture

content of the precipitation, wind, or aircraft skin temperature.

The operational use of holdover timetables is not mandatory for

FAR Part 135 operations unless the operator elects to comply and

the FAA approves its compliance with the FAR Part 121 ground

deicing/anti-icing rule requirements.  Holdover timetables

provide information on the effectiveness of deicing/anti-icing

fluids and should be used for departure planning and coordination

purposes in conjunction with pretakeoff contamination check

procedures.  Operations manuals and operations specifications

should contain detailed procedures for conducting the pretakeoff

contamination check as well as the procedures for using the

holdover timetables.

b.  Development of Holdover Timetables.  Holdover

timetables have been developed by the SAE and ISO.  Each

certificate holder may develop their own holdover timetables for

use by its personnel, but the timetables must be supported by

data acceptable to the Administrator;  currently, the SAE/ISO

holdover timetables are considered by the FAA to be the only

acceptable data for use by FAR Part 121 certificate holders.

This policy will also apply to FAR Part 135 certificate holders

(see Appendix A, Tables 1 and 2).  Further guidance regarding

holdover timetables is contained in AC 20-117, AC 120-58, AC 135-

17, SAE ARP 4737, and ISO 11076.

12.  AIRCRAFT DEICING/ANTI-ICING PROCEDURES, INCLUDING

INSPECTION AND CHECK PROCEDURES AND RESPONSIBILITIES.  Deicing

and anti-icing procedures must be specific to each aircraft type

in accordance with FAR Section 135.345.  Those aircraft-specific

procedures should include instructions and checking guidelines

for use by their pilots, and if appropriate and authorized, other

personnel to determine whether or not aircraft surfaces are free

of contaminants.  Those aircraft-specific instructions and

guidelines should also be in the certificate holder's operations

manual, and described or referenced in their operations

specifications.

a.  Deicing/Anti-Icing Procedures.  Deicing/anti-icing

procedures should include, as applicable to each certificate

holder:

(1) Methods of deicing (e.g., warm hangar, deicing

fluid).

(2) Safety requirements during fluid application.

(3) Aircraft-specific considerations.

(4) Location-specific procedures.

(5) Post deicing/anti-icing checks.

(6) Contractor Deicing.  Many certificate holders

will utilize contract services, such as aircraft servicing

vendors, fixed base operators, or other air carriers to perform

deicing/anti-icing.  If such is the case, the certificate

holder's training program should include training for contractors

and/or the PIC's responsibilities for supervising a contractor

who provides deicing/anti-icing services.

b.  Deicing/Anti-Icing Checking Procedures and

Responsibilities.  The certificate holder's training program

should have pilot training on aircraft-specific surface

contamination checking to include the following:

(1) Pilot Preflight Inspection/Cold Weather Preflight

Inspection Procedures.  This is the normal walkaround preflight

inspection conducted by a pilot.  This inspection should be used

to note any aircraft surface contamination and to direct any

required deicing/anti-icing operation.

(2) Pretakeoff Contamination Check.  An aircraft

check completed within 5 minutes prior to beginning takeoff to

make sure the wings and control surfaces are free of

contamination.  Each carrier must define the content of the

pretakeoff contamination check.  The check may be conducted from

inside or outside the aircraft, depending upon such factors as

atmospheric conditions, lighting conditions, aircraft type and

ability of the crew to see the relevant aircraft surfaces.

(3) Certificate holders should consider the following

guidelines for obtaining approval to conduct the pretakeoff

contamination checks from inside the aircraft.

(i) Can enough of the surfaces be seen to

adequately determine whether or not the wings and control

surfaces are free of contaminants?  This determination should

consider the aircraft type, the method of conducting the check-

that is, from the cockpit or cabin; lighting; and atmospheric

conditions.

(ii) Does the certificate holder have procedures

to recognize, and has the pilot been properly trained to

recognize changes in weather conditions to allow the PIC to

ascertain whether or not the wings and control surfaces could

reasonably be expected to remain free of contaminates?

c.  Alternative Procedure.  The Administrator may approve

a certificate holder's alternative procedure, which ensures that

wings and control surfaces are free of frost, ice, or snow,

instead of a pretakeoff contamination check.  An alternative

procedure may include procedures, techniques, or equipment (such

as wing icing sensors) to establish that wings and control

surfaces are not contaminated.  Any alternative procedure should

be approved by the certificate holder's POI through the Manager,

Air Transportation Division, AFS-200, and after approval,

detailed in the operator's training program (if applicable),

operations manual (if applicable), and described or referenced in

its operations specifications.

d.  PIC Responsibility.  Operator-developed guidance and

procedures should contain a discussion regarding the PIC's

responsibility to make the decision on whether or not to take

off.

e.  Aircraft Surfaces.  The aircraft surfaces, which

should be clear of contaminants before takeoff, should be

described in the aircraft manufacturer's maintenance manual or

other manufacturer-developed documents, such as service or

operations bulletins.

(1) For each type of aircraft used in their

operations, certificate holders should explain in their training

programs and list in their operations manual (which are

referenced in the operations specifications) those surfaces which

should be checked during preflight inspections and pretakeoff

contamination checks.

(2) Generally, the following aircraft surfaces should

be clear of contaminants, if the aircraft manufacturer's

information is not available:

(i) Propeller, windshield, wing, empennage,

stabilizing, and control surfaces.

(ii) Powerplant installation(s), including

associated surfaces and systems such as engine inlets and fuel

vents.

(iii) Airspeed, altimeter, rate of climb, and

flight attitude instrument, including associated surfaces or

systems such as pitot heads, static ports, and instrument sensor

pickup points.

13.  COMMUNICATIONS.

a.  Before beginning the deicing/anti-icing procedures,

the PIC should:

(1) Coordinate with air traffic control (ATC) for

departure planning.

(2) Obtain the most current weather information.

b.  When deicing/anti-icing with fluids is accomplished,

the PIC should have the following information:

(1) Fluid type (for example, Type I or Type II).

(2) Fluid/water mix ratio.

(3) Start time of final fluid application/beginning      			     of holdover time.

(4) Verification that the aircraft is free of      				     contamination.

14.  AIRPLANE SURFACE CONTAMINATION.

a.  Certificate holders should include training which

ensures that pilots are knowledgeable in the following:

(1) Freezing Precipitation.  Snow, sleet, freezing

rain, drizzle, or hail which adheres to aircraft surfaces.

(2) Frost, Including Hoarfrost.  Hoarfrost is a

deposit of interlocking ice crystals formed by direct sublimation

of water vapor on an object or aircraft surface, which is at or

below 0 deg. C (32 deg. F).

(3) Freezing Fog.  Clouds of supercooled water

droplets that form a deposit of ice on objects in cold weather

conditions.

(4) Snow.  Precipitation in the form of small ice

crystals or flakes which may accumulate on or adhere to aircraft

surfaces.

(5) Freezing Rain.  Water condensed from atmospheric

vapor falling to earth in supercooled drops, forming ice on

objects.

(6) Rain or High Humidity (on Cold-Soaked Wing).

Water forming ice or frost on the wing surface when the

temperature of the aircraft wing surface is at or below 0 deg. C

(32 deg. F).  This ice or frost may freeze over the entire wing

surface and on the wing leading edge.  Some aircraft may be

susceptible to the formation of frost or ice on wing surfaces

when the wing surfaces are cold-soaked and the aircraft is

exposed to conditions of high humidity, rain, drizzle, or fog at

ambient temperatures above freezing.

(7) Underwing Frost.  Takeoff with frost under the

wing in the area of the fuel tanks (caused by cold-soaked fuel)

within limits established by the aircraft manufacturer,

authorized by FAA aircraft certification offices, and stated in

aircraft maintenance and flight manuals may be permitted.

b.  Effects of Frost, Ice, Snow, and Slush on Aircraft

Performance, Stability, and Control.  The certificate holder

should obtain this information from the manufacturer of each type

of aircraft it uses in its operations and should ensure that its

pilots are trained in the following effects of contamination on

aircraft performance.

(1) Increased drag/weight.

(2) Tendency for rapid pitch-up during rotation or

wing roll off.

(3) Loss of lift.

(4) Stall occurs at lower-than-normal angle of      				     attack.

(5) Buffet or stall occurs before activation of

stall warning.

(6) Decreased effectiveness of flight controls.

15.  TYPES AND CHARACTERISTICS OF DEICING/ANTI-ICING FLUIDS.

(a)  Certificate holders should refer to the SAE and ISO

publications in paragraphs 3(f) and 3(g) for additional

information on specific deicing and anti-icing methods and

procedures and on fluid characteristics and capabilities.

(b)  If the certificate holder intends to use

deicing/anti-icing fluids for ground deicing, the types and

characteristics of deicing/anti-icing fluids should be included

in the certificate holder's training program and operations

manual.  Deicing and anti-icing fluids with differing

characteristics and capabilities exist; they may undergo

improvements, and new types of fluids may be developed.

Certificate holders should ensure that their pilots are

knowledgeable about the characteristics of each type of fluid

used.

(c)  Certificate holders should ensure that the following

subjects are discussed, as applicable:

(1) Deicing Fluids.

(i) Heated water.

(ii) Heated mixtures of water and SAE/ISO Type I

fluid.

(iii) Heated mixtures of water and SAE/ISO Type II

fluid.

Note:  Deicing fluid should be applied heated to assure maximum efficiency.

(2) Anti-Icing Fluids:

(i)   Mixtures of water and SAE/ISO Type I fluid.

(ii)  SAE/ISO Type II fluid.

(iii) Mixtures of water and SAE/ISO Type II fluid.

Note:  SAE/ISO Type II anti-icing fluid is normally applied cold on clean aircraft surfaces, but may be applied heated.  Cold SAE/ISO Type II fluid normally provides longer anti-icing protection.  SAE/ISO Type I anti-icing fluid should be applied heated and diluted.

(3) Unapproved Fluids and Antifreeze.  Use freezing

point depressant (FPD) fluids approved for use by the aircraft

manufacturer.  Some fluids may not be compatible with aircraft

materials and finishes and some may have characteristics that

impair aircraft performance and flight characteristics or cause

control surface instabilities.  Use of automotive antifreeze for

deicing is not approved.  Its holdover time and its effects on

aircraft aerodynamic performance are generally unknown.

c.  Fluid Characteristics.

(1) Type I Fluids.

(i) Unthickened.

(ii) Limited holdover time.

(iii) When applied, forms thin liquid film on 					   wing.

(2) Type II Fluids.

(i) Thickened.

(ii) Longer holdover times in comparison to those

of Type I fluids.

(iii) Application results in a thick liquid film

(a gel-like consistency) on wing.

(iv) Windflow over the wing (shear) causes the

fluid to progressively flow off the wing 					   during takeoff.

(3) Deicing/Anti-Icing Fluids Handling/Performance

Implications.  The type fluid used and how completely the fluid

flows off the wing during takeoff determines the effects of the

following handling/performance factors.  The aircraft

manufacturer may also provide performance information regarding

the use of the different deicing/anti-icing fluids.

(i) Increased rotation speeds/increased field

length.

(ii) Increased control (elevator) pressures on

takeoff.

(iii) Increased stall speeds/reduced stall

margins.

(iv) Lift loss at climbout/increased pitch

attitude.

(v) Increased drag during acceleration/increased

field length.

(vi) Increased drag during climb.

16.  COLD WEATHER PREFLIGHT INSPECTION PROCEDURES.

a.  Pilot Preflight Inspection/Cold Weather Preflight

Inspection Procedures.  This is the normal walk-around preflight

inspection conducted by a pilot.  This inspection should be used

to note any aircraft surface contamination and initiate any

required deicing/anti-icing operations.

b.  A thorough preflight inspection is more important in

temperature extremes because those temperature extremes may

affect the aircraft or its performance.  At extremely low

temperatures, the urge to hurry the preflight of the aircraft is

natural, particularly when the aircraft is outside and adverse

weather conditions exists, which make the preflight physically

uncomfortable for the pilots.  This is the very time to perform

the most thorough preflight inspection.

c.  Aircraft areas that require special attention during

a preflight inspection during cold weather operations depend on

the aircraft design and should be identified in the certificate

holder's training program.  The preflight should include all

items recommended by the aircraft manufacturer.  A preflight

should include items appropriate to the specific aircraft type.

Generally, those items may include:

(1) Wing leading edges, upper and lower surfaces.

(2) Vertical and horizontal stabilizing devices,

leading edges, upper surfaces, lower surfaces, 				     and side panels.

(3) Lift/drag devices such as trailing edge flaps.

(4) Spoilers and speed brakes.

(5) All control surfaces and control balance bays.

(6) Propellers.

(7) Engine inlets, particle separators, screens, and

pressure probes.

(8) Windshields and other windows necessary for

visibility.

(9) Antennas.

(10) Fuselage.

(11) Exposed instrumentation devices such as

angle-of-attack vanes, pitot-static pressure 				     probes, and static ports.

(12) Fuel tank and fuel cap vents.

(13) Cooling and auxiliary power unit (APU) air

intakes, and exhausts.

(14) Landing gear.

d.  Blowing Snow.  If an aircraft is exposed to blowing

snow, special attention should be given to openings in the

aircraft where snow can enter, freeze, and obstruct normal

operations.  The following openings should be free of snow and

ice before flight:

(1) Pitot tubes and static system sensing ports.

(2) Wheel wells.

(3) Heater intakes.

(4) Engine air intakes and carburetor intakes.

(5) Elevator and rudder controls.

(6) Fuel vents.

17.  TECHNIQUES FOR RECOGNIZING CONTAMINATION ON THE AIRPLANE.

a.  Certificate holders should have aircraft-specific

techniques for the use of their pilots (and other 				personnel, if

applicable) to recognize contamination on aircraft 				surfaces and indications of loss of effectiveness of 				fluids.

b. Some indications for loss of effectiveness of 					deicing/anti-icing fluid or contamination on aircraft 			surfaces include:

(1) Progressive surface freezing or snow 					     accumulation.

(2) Random snow accumulation.

(3) Dulling of surface reflectivity (loss of gloss)

caused by the gradual deterioration of the fluid 			     to slush.

(4) Fluid characteristics and indications that the

fluid is losing its effectiveness obtained from 				     the deicing/anti-icing fluid manufacturers.

/s/ William J. White

Deputy Director, Flight Standards Service